IMPORTANT DRIVE CHAIN INFORMATION / 56031-1157
To prevent an accident and/or damage to the motorcycle, the drive chain / must be properly maintained. It should be lubricated every 300km (200mi) / and adjusted as often as necessary to keep chain slack at about 30 ~ 35 mm / (1.2~1.4in) with the motorcycle on the center stand. See the Owner's Manual / for chain care and adjustment information. / The standard chain is an Enuma EK630SADO with estimated service life of / 15,000~45,000km (10,000~30,000mi),depending on the severity of use / and the frequency of lubrication and adjustment. For safety, replace the chain / with only the standard chain any time is wears over 389 mm (15.3in), / measured over a 20-link portion pulled straight with 10 kg (20lbs) of / tension. See the Owner's Manual for chain replacement procedure.